## Slide 1: Implementation and STA
Artix-7
Vivado 2017.1 Version
Notes: Implementation takes a netlist and maps it into the physical array of a Xilinx device.

## Slide 2: Objectives
After completing this module, you will be able to:
  Implement a design to completion
  Generate useful implementation reports
  Describe static timing analysis and static timing paths
  Describe setup and hold checks
  Understand the relationship between clocks and setup and hold checks
  Generate a custom timing report to perform basic static timing analysis
  Use the timing summary report to verify your timing constraints were met
  Generate a bitstream and verify the functionality in hardware

## Slide 3: Outline
Implementation
Reports
Basic Static Timing Analysis
Bitstream Generation and Verification in Hardware
Summary

## Slide 4: Implementation: ISE vs. Vivado
Notes: This table highlights the differences between implementation commands/operations in Vivado and ISE.
As we can see, Vivado breaks the implementation flow down into more operations than ISE.

## Slide 5: opt_design: Logic Optimization
Ensures optimal netlist for placement
  Further logic optimization on fully-assembled netlist built from synthesized RTL, IP blocks
    Performs logic trimming on incoming netlist
    Constant propagation – remove unnecessary static logic
    LUT equation remapping
Optional in non-project batch flow (but recommended)
  Example: needed to trim unused bank cells in MIG IP (phaser/iodelay/….)
Automatically enabled in the project-based flow
Notes: Because this is the first view of the assembled design (RTL and IP blocks), the design can usually be further optimized. The opt_design command is the next step and performs logic trimming, removing cells with no loads, propagating constant inputs, and combining LUTs for example LUTs in series that can be combined into fewer LUTs.
Constant propagation: Propagates constant values through logic which results in:
Obsolete logic – example: a logic AND with a logic 0 input
Reduced logic – example: a 3-input OR with a logic 1 input reduced to a 2-input OR
Redundant logic – example: a 2-input OR with a logic 1 input is reduced to a wire
Remap: Combines multiple LUTs into a single LUT to reduce the depth of the logic.

## Slide 6: opt_design Options
Non-project batch flow
  Can specify which optimizations to perform from a script
Notes: Optimizes a design netlist for the target part. Optimization can provide improvements to synthesized netlists from third-party tools, or for netlists that may not have been optimized during synthesis.
Run this command prior to implementation to optimize the design and simplify the netlist before placing and routing the design.
The opt_design command performs the following optimizations by default:
* Retarget
* Constant Propagation
* Sweep
* Block RAM Power optimizations

## Slide 7: power_opt: Power Optimization
Power optimization includes a fine-grained clock gating solution that can reduce dynamic power by up to 30%
Intelligent clock gating optimizations are automatically performed on the entire design and will generate no changes to the existing logic or clocks
Algorithm performs analysis on all portions of the design
  Legacy and third-party IP blocks

## Slide 8: Power Optimization Commands
Automatic power reduction
  Automatically turns off unused portions of the design
  Does not require deep system level knowledge
Vivado IDE provides optimization control at global and object level
  Global command for optimizing the design: power_opt_design
  Local level control through SDC command: set_power_opt
    Instance level: Include/exclude instances for power opt
    Clock domain: Optimize instances clocked by the specified clock
    Cell-type level: Block RAM, registers, SRL

## Slide 9: place_design: placer
Project-based flow
  Included in implementation stage
Non-project batch flow
  place_design
Can use an input XDEF as a starting point for placement

## Slide 10: Placement
Phases of a complete placement
  Pre-placement DRC
    Check for unroutable connections, valid physical constraints, overutilization
  Placement
    I/O and clock placement
Macro and primitive placement
  Timing-driven and wire length-driven
  Congestion-aware
Detailed placement
  Refine locations of small "shapes," flip-flops, LUTs
  Commit to location sites – pack into slices
Post-commit optimizations
Notes: The next step after logic optimization is placement. These are the major phases of a full placement. For global placement, the placer builds shapes ahead of time.
Placement is not clock skew aware. Skew is included with timing, but it does not target the skew as being too large and optimize placement to minimize clock skew. But it does include skew with the timing information used during placement.
The tools spend a lot more time trying to meet a hold violation because design will not run if there is a hold violation.

## Slide 11: phys_opt_design: Physical Synthesis
Post-placement timing-driven optimization
  Replicates and places drivers of high fanout nets with negative slack
    Replication only performed if it improves timing
    Slack must be within critical range
      Approximately 10% of worst negative slack (WNS)
Available in all flows and can be de-activated in the GUI
  phys_opt_design
  Run between place_design and route_design

## Slide 12: route_design: Router
Project-based flow
  Included in implementation stage
Non-project batch flow
  route_design
Router reporting
  report_route_status command
  Check route status of individual nets
    Fully routed: lists routing resources
    Failed routes

## Slide 13: Router
Phases of a complete route
  Special net and clock routing
  Timing-driven routing
    Prioritized by setup/hold path criticality
    Swap LUT inputs pin to improve critical paths
    Fix reasonable hold time violations
Two modes
  Normal (default): Router starts with a placed design and attempts to route all nets
  Re-Entrant (non-project batch only): Router can route/unroute as well as lock/unlock specific nets
Notes: The router can start with either a placed, unrouted design or a routed design with some or all nets routed. The router then allows any amount of incremental routing changes. This mode is used to control routing of a subset of nets.

## Slide 14: Outline
Implementation
Reports
Basic Static Timing Analysis
Bitstream Generation and Verification in Hardware
Summary

## Slide 15: After Implementation
Sources and Netlist tabs do not change
  As each resources is selected, it will show the exact placement of the resource on the die
Timing results have to be generated with the Report Timing Summary
As each path is selected, the placement of the logic and its connections is shown in the Device view
  This is the cross-probing feature that helps with static timing analysis

## Slide 16: Implementation Reports
While the Flow Navigator points to the most important reports, the Reports tab contains several other useful reports
  Post Optimization DRC Report: Lists the I/O DRC checks that were completed
  Post Power Optimization DRC Report: Lists the power DRC checks that were completed
  Place and Route Log: Describes the implementation process and any issues it encountered
  IO Report: Lists the final pinout for your design
  Clock Utilization Report: Describes the clock resources used and the clock utilization resource on a region-by-region basis
  Utilization Report: Describes the amount of FPGA resources used in a text format
  Control Sets Report: describes how your control signals were grouped

## Slide 17: Utilization Reports
Double-click in the Reports tab to view in text form
Click on Report Utilization under Implementation Result in the Flow Navigator pane to view in chart/table format

## Slide 18: I/O Report
This report provides a table that lists every signal, its attributes, and its final location
  It is always important to double-check pin assignments before implementing because the tools can move any pin that is unassigned

## Slide 19: Clock Utilization Report
This report describes the clocking resources used in the design
  BUFG, BUFH, BUFHCE, MMCM, and a clock region analysis

## Slide 20: Control Sets Report
This report describes the number of unique control sets in the design (ideally this will be as small as possible)
Number of control sets describes how control signals were grouped
  This determines the ability of the tools to reach high device utilization
  Number of controls signals in the design is determined by the designer's inference of sets, resets, and clock enable signals
  Number of control signals can be reduced if the designer attempts to share controls signals throughout the design as much as possible
Notes: Control signals include clocks, clock enables, set, and reset signals. How the tools group them into slices and CLBs will dictate the density (efficiency) of the design in the FPGA.
Xilinx recommends using synchronous sets/resets whenever possible and that designers reduce the number of control signals in their design to improve device utilization.

## Slide 21: power_opt: Report
report_power_opt command details the gating performed on the design by the power_opt program
  Can be run before power optimization to create a report detailing all the user-gated logic in the design for a before and after picture of your design

## Slide 22: Outline
Implementation
Reports
Basic Static Timing Analysis
Bitstream Generation and Verification in Hardware
Summary

## Slide 23: Static Timing Analysis (STA)
A design is an interconnected set of cells and nets
The functionality of a design is determined by the RTL design sources
  The functionality can be verified by a simulation tool
The performance of a device is determined by the delays of the cells that comprise the design
  This is verified by static timing analysis
In STA the functionality of the components of the design are not important
  Only the performance of the components
  Cells need only be classified as combinatorial or sequential

## Slide 24: Component Delays
Each component takes time to perform its function
  A LUT has propagation delay from its inputs to its outputs
  A net has propagation delay from the driver to the receiver(s)
  A flip-flop requires stable data for a required time around its sample point
These delays are dependent on a several factors
  Some are determined by the composition of the FPGA and the implementation of the design
    The physical characteristics of the element (how it is constructed)
    The location of the object (where it is placed with respect to other objects)
  Some are determined by environmental factors (PVT)
    The process variation of the device
    The voltage applied to the cells
    The temperature of the cells

## Slide 25: Delays
Component and net delays are provided by Xilinx, and are extracted by careful characterization of production devices
  Timing is extracted over the allowed operating range of the device
    Process is within a specific range
      Different ranges are used for different speed grades (-1, -2, -3)
    Voltage is between the minimum and maximum allowed for the device
      Different speed grades may allow different voltages (i.e. -1L)
    Temperature is between the maximum and minimum specified
      Commercial and industrial parts allow different temperature ranges
  These characterized delays may be extracted at various process corners
  Fastest PVT, slowest PVT
  The characterized delays at the appropriate corner are used by the tools during STA

## Slide 26: Why Do We Need STA?
Many of the processes in FPGA implementation are timing driven
  Synthesis for circuit construction
  Placer for optimal cell locations
  Router for choosing routing elements
Tools must have constraints to determine the desired performance goals
STA is used during the processes, and afterwards for generating reports
Ultimately, STA determines if a design will provide the desired performance

## Slide 27: report_timing_summary: Timing Report Summary
Timing reports with true timing information can be generated from the Flow Navigator after implementation has been completed

## Slide 28: Timing Summary
Summary reports Setup, Hold, and Pulse Width related results
  Setup
    Worst Negative Slack (WNS): The worst slack of all the timing paths for max delay analysis. It can be positive or negative; positive means no violation
    Total Negative Slack (TNS): The sum of all WNS violations, when considering only the worst violation of each timing path endpoint- 0ns when all timing constraints are met, Negative when there are some violations
    Number of Failing Endpoints: The total number of endpoints with a violation (WNS<0ns)
  Hold
    Worst Hold Slack (WHS): Corresponds to the worst slack of all the timing paths for min delay analysis. It can be positive or negative
  Pulse Width
    Worst Pulse Width Slack (WPWS): Corresponds to the worst slack of all the timing checks listed above when using both min and max delays

## Slide 29: The Timing Summary Table
The Timing Summary table shows
  General Information provides design name, device, package, speed grades etc.
  Timer Settings provides timing analysis engine settings
  Design Timing Summary provides a summary of all the timing reports
  Clock Summary includes information similar to that produced by report_clocks
  Check Timing includes information about missing timing constraints or paths with constraints issues that need to be reviewed
  Intra-Clock Paths includes summary of the worst slack and total violations of the timing paths with the same source and destination clocks
  Inter-Clock Paths includes summary of the worst slack and total violations of timing paths with different source and destination clocks
  Other Path Groups displays paths not covered above, including user-defined path groups
  User Ignored Paths are paths that are ignored during timing analysis
  Unconstrained Paths contain paths that were not covered by the XDC constraints
  Violations are displayed in red

## Slide 30: Static Timing Paths
A static timing path is a path that
  Starts at a clocked element
  Propagates through any number of combinatorial elements and the nets that interconnect them
  Ends at a clocked element
Clocked elements include flip-flops, block RAMs, DSP cells, …
Combinatorial elements include LUTs, wide MUXes, carry chains, …

## Slide 31: Setup Check
Checks that a change in a clocked element has time to propagate to other clocked elements before the next clock event
  That is, from the rising edge of the clock to the next rising edge of the clock
  Checked for all static timing paths

## Slide 32: Hold Check
Checks that a change in a clocked element caused by a clock event does not propagate to a destination clocked element before the same clock event arrives at the destination element
  Usually from the rising edge of the clock to the same edge of the clock
  Checked for all static timing paths
The shortest delay is used for Source Clock and Data Path Delay, and the longest delay is used for Destination Clock Delay

## Slide 33: report_timing_summary: TRCE Like Report
report_timing_summary command produces a comprehensive TRCE-like timing report
This report contains these sections
  Timer Settings
  check_timing report
  Design Timing Summary
  Clock Definitions
  Intra Clock table
  Inter Clock table
  Path Group table

## Slide 34: Anatomy of Timing Report

## Slide 35: Report Sections
Report summary
Design timing summary
Clock summary

## Slide 36: Report Sections
Intra clock table
Maximum delay path

## Slide 37: Report Sections
Delay path

## Slide 38: Outline
Implementation
Reports
Basic Static Timing Analysis
Bitstream Generation and Verification in Hardware
Summary

## Slide 39: Bitstream Generation
Generates bitstream for the device chosen for the current project
Runs on an implemented design
Uses the pull model to regenerate implemented design if design is out of date
Project-based flow
  IDE: Generate bitstream
  Tcl: launch_runs impl_1 -to_step write_bitstream

## Slide 40: Bitstream Generation Settings
By default binary bitstream format is used
-raw_bitfile: Causes write_bitstream to write a raw bit file (.rbt) containing the same information in ASCII format
-mask_file: Generates a mask file that masks out dynamic bits in the device fabric
-no_binary_bitfile: Do not write the binary bitstream file (.bit)
  Use this command to generate the ASCII bitstream or mask file, or to generate a bitstream report, without generating the binary bitstream file
-bin_file: Creates a binary file (.bin) containing only device programming data, without the header information
-logic_location_file: Generates a (.ll) file that contains the location of LUTs, BRAM, flip-flops, latches, I/O block inputs and outputs

## Slide 41: Hardware Manager
The steps to connect to hardware and programing the target FPGA device
  Open a hardware manager
    Uses Target Communication Framework (TCF) Agent, hw_server
  Open a hardware target that is managed by a hardware server running on a host computer
  Associate the bitstream data programming file with the appropriate FPGA device
  Program or download the programming file into the hardware device
  Opens the hardware analyzer view for debugging

## Slide 42: Outline
Implementation
Reports
Basic Static Timing Analysis
Bitstream Generation and Verification in Hardware
Summary

## Slide 43: Summary
Implementation is made up of the programs link, opt_design, power_opt, place_design, phys_opt_design, and route_design
There are several implementation reports available to help designers better manage their FPGA designs
Static timing paths start at clocked elements and end at clocked elements
Static timing paths are analyzed for setup and hold violations at both fastest and slowest process corners
Setup and hold checks include the analysis of the clock propagation paths
report_timing_summary is used as post-implementation sign-off
report_timing is used for interactive and detailed timing analysis after synthesis or implementation