## Slide 1: Xilinx Design Constraints
Artix-7
Vivado 2017.1 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Assign pin locations using the I/O Planner
  Describe static timing paths
  Create real and virtual clocks
  Create appropriate input and output delays
  Use virtual clocks for input and output delays
  Use the Constraints Wizard

## Slide 3: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 4: Pin and Clock Planning
Pin and clock planning often happens early in the project
  Decisions here can have significant effects throughout the design
    Excessive clock skew
    Poor I/O timing
    Timing-hazardous clock domain crossing
    Less flexible design placement
    Fewer clocking resource choices
    Poor logic placement
    Excessive routing delays
    Reduced device utilization
Pin and clock planning should be considered together
  Choices made for clock pins affect clocking timing and resources choices
  Choices made for data pins affect clock pin placement decisions

## Slide 5: Design View Layouts
Several default view layouts available
  Toolbar pull-down (I/O Planning, Clock Planning, Floorplanning, etc)
Designs load with "Design Analysis" view by default
Use "I/O Planning" for easy access to I/O planning functions
  Adds Package view, clock resources, I/O ports, package pins

## Slide 6: I/O Planning Project
When creating a new project from the Getting Started page you have the option to create an I/O planning project without RTL
  This allows testing of pin assignments
    I/O banking rules
    Avoid ground bounce
    The I/O Planner performs error checking for your pinout
  However, it is recommended that you have RTL associated
    Error checking is better
Notes: The New Project Wizard presents four project types of choices. Choosing an I/O planning project when there is not a netlist or RTL allows you to build a prototype pinout and test it. However, it is preferred that you have RTL associated with your project when you start to make your pin assignments. This is because the error checking is more thorough when you have RTL.
I/O pin planning projects always open in the I/O Planning view.
An XDC file is a user constraints file and is designed to store your pin assignments and pin attributes. It can also be used to store your design’s timing constraints. The Vivado IDE software also allows you to modify your design’s timing constraints.

## Slide 7: Launching I/O Planner with RTL
This flow is used if you already have a RTL project created
  Synthesize the design
    Open synthesized design by clicking Open Synthesized Design
    Open the I/O Planner by selecting the I/O Planning view from the drop-down box on the horizontal toolbar
      This allows you to view and/or enter the I/O locations and properties
Notes: If you already have logic associated with your project, you will not be using the Create an I/O Planning Project option from the New Project Wizard. Instead, you will simply open an existing project and open the I/O Planner this way.

## Slide 8: I/O Planner
I/O Planner performs error checking on the design pin layout
  This requires rules-based I/O assignments
    DRC provides guidance for pin assignments connecting to dedicated FPGA logic (microprocessor, MGT, or differential pairs, for example)
    Noise analysis (to avoid ground bounce)
    Verify I/O banking rules
  Semi or fully automatic pin assignment capabilities
    Xilinx recommends that you place timing-critical ports before allowing automatic pin assignment of the remaining pins
  Supports grouping-related pins to simplify I/O interface management

## Slide 9: I/O Planner Layout View
I/O Planner allows you to view both the Die and Package views so that you can understand the I/O bank relationship with your logic
Package and Device views
  Graphically displays package pins, die pads, and I/O banks
  I/O ports can be assigned within either of these two views
Package Pins view
  Displays I/O package specifications and assignment status
    Allows you to see the Trace delays, pin type, voltage standard, and differential pair partners
  Can display pins as a group, in an I/O bank, or as a list
  As you drag across the display, icons show pin and I/O bank placement status
Notes: As pins or banks are selected, the corresponding pins or banks become highlighted in the other views. This makes it easy to see that the pins assigned in each bank meet the I/O banking rules and are grouped appropriately.
Clock pins are shown as gray hexagons, clock-capable pins are shown as blue hexagons, power pins are shown as red squares, and ground pins are shown as green squares. These views also allow you to manually assign I/O-related objects, such as BUFRs, BUFGs, IODELAYCTRLs, or MGTs.
When pins are displayed as a list they can be easily sorted. This allows you to see them organized by attributes such as prohibited pins.
As you drag across the package view, yellow icons indicate assigned pins, gray icons indicate unassigned pins, and both displayed indicates partially assigned I/O banks.

## Slide 10: Package View
The colored areas between the pins display the I/O banks
Show differential pairs
Clock-capable pins ( ), VCC ( ), GND ( ), no connection ( ), XADC ( ), Temperature Sensor ( )
Notes: In the package view:
Clock-capable pins display as hexagon pins
VCC and GND pins show as red and green square pins
The colored areas between the pins display the I/O banks
The Package View Layers option allows you to turn on/off pins of a certain type.
Moving and holding the cursor over the display will show the pin information.
Ports and I/O buffers can be dragged into the Package view or Device view for assignment

## Slide 11: set_property command
Use set_property command
  set_property PACKAGE_PIN T22 [get_ports led_pins[0]]
  set_property IOSTANDARD LVCMOS33 [get_ports led_pins[0]]
  Or
  set_property -dict {PACKAGE_PIN H17 IOSTANDARD LVCMOS33} [get_ports { led_pins[0] }]

## Slide 12: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 13: Static Timing Paths and I/O
Static timing paths start at clocked elements and end at clocked elements
  Paths from internal flip-flop to internal flip-flop are constrained by clock
Inputs and outputs of the FPGA are not start-points/end-points of static timing paths
  By default, any logic between a primary I/O and an internal clocked element are not part of a complete static timing path
  Without additional commands, no setup/hold checks are done on logic associated with I/O

## Slide 14: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 15: Clocks
Clocks are periodic signals
Clocks have certain attributes
  Period
    Nominal time from rising edge of the clock to the next rising edge of the clock
  Duty cycle
    Ratio of the high time to the low time of the clock
  Jitter
    Variation of the period from its nominal value
  Phase
    Position of the rising edge

## Slide 16: Clocks as Objects
In XDC clocks are primary objects
Clocks have properties
  NAME is the name of the clock
    Will be user assigned or auto generated depending on the clock
  PERIOD is the period of the clock
  WAVEFORM describes the position of the edges of the clock
  IS_GENERATED, IS_VIRTUAL are flags that describe how the clock was created
  SOURCE_PINS are the pins/ports/nets which the clock is attached to

## Slide 17: Creating Clocks
Clocks are created with the create_clock Tcl command
  create_clock -name <name> –period <period> <objects>
  <period> is the period of the clock
  <name> is the user assigned name for the clock
  <objects> are the list of pins, ports, or nets to which to attach the clock
  If <objects> is not present (or is a null list), the clock will not be attached to any objects, and will be a virtual clock
create_clock –name my_clock –period 5.0

## Slide 18: Clock Waveform
Clocks can be created with edges at different positions
  Allows for the description of clocks with phase offsets and clocks with different duty cycles
  Uses the –waveform <edges> option
    <edges> is a list of numbers representing the times of successive edges
      The first number is the time of the first rising edge
    Default is 0.00 for the rising edge and PERIOD/2 for the falling edge
create_clock –name clk2 –period 5.0 –waveform {1.0 4.0}
Notes: As with all Tcl commands, variables and expressions can be used for any options. Therefore, to define the above clock using an offset and duty cycle could be done as follows:
set period 5.0
set offset 1.0
set duty_cycle 0.6
create_clock -name clk2 -period $period -waveform "$offset [expr $offset + $period * $duty_cycle]"
Note the use of the “” to enclose the list, rather than {}. Inside {} variables are not expanded and embedded commands are not processed.

## Slide 19: Setting Jitter
The Vivado Design Suite timing engine allows for two sources of jitter
  System Jitter: Jitter introduced by the clocking network inside the FPGA
    A single value for all clocks in the system
    Set with the set_system_jitter command
    set_system_jitter <value>
      <value> is the jitter in time units (nanoseconds)
  Input Jitter: Jitter that exists on the input clock
    Set independently for each clock source
    Set with the set_input_jitter command
    set_input_jitter <clock_name> <value>
      <clock_name> is the name of a clock (not the clock object)
      <value> is the jitter in time units
Both sources of jitter will be combined appropriately in STA calculations
Notes: The set_input_jitter command takes a clock name as an option. In this command (and a few others) the actual name of the clock is used, rather than the object itself. Thus, you can use:
set_input_jitter clk_pin_p 0.2
For this command, the get_clocks is assumed. However, it is still legal to use it; the following command is equivalent:
set_input_jitter [get_clocks clk_pin_p] 0.2

## Slide 20: Clock Latency
The latency of the clock can be controlled with the set_clock_latency Tcl command
  set_clock_latency –source <latency> <objects>
  <latency> is the latency to apply
  <objects> is the list of clocks, ports or pins to which to apply the latency
The latency is an additional clock delay that is added between the clock object and the pin, port, or net to which the clock is attached
  If the set_clock_latency specifies a clock object, the latency is added to all destinations of the clock
  If the set_clock_latency specifies a port or pin, it applies to all clocks that go through that port or pin
    If the port or pin has more than one clock associated with it, the –clock <clocks> option can be used to specify which clocks to apply the latency to

## Slide 21: Options of the set_clock_latency Command
The set_clock_latency command has several options
  -rise: The specified latency applies only to the rising edge of the clock
  -fall: The specified latency applies only to the falling edge of the clock
  -min: Specifies the latency to apply when the shortest path is used
  -max: Specifies the latency to apply when the longest path is used
If the –min/-max are not specified, the latency applies to both min and max
If the –rise/-fall are not specified the latency applies to both rise and fall

## Slide 22: Creating Clocks using the GUI
The Timing Constraint window can be opened using the menu Window > Timing Constraints
  A clock can be created by double clicking on the Create Clock, or a new row in the Create Clock table
Alternatively can be set via the Constraints Wizard
  Covered later in this presentation

## Slide 23: The Create Clock Wizard
Name of clock to be created
Objects to which attach clock
Period and edges of the clock
Tcl command to create clock

## Slide 24: Handling Clock Objects
Clocks can be attached to pins, ports, and nets
  Specify the list of pins, ports, or nets which are to be attached to the clock when the clock is created
Once created, clock objects can be gotten using the get_clocks command
  get_clocks <name>
    Returns list of clocks that match <name>
    <name> may include wildcards
  Has similar options as the other get_* commands
    -regexp
    -filter <expression>
    -of_objects <object>

## Slide 25: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 26: Synchronous Input Interfaces
Most interfaces to an FPGA use synchronous communication
  FPGA and the device driving the FPGA have some shared timing reference
    This is usually a common clock or a related clock
Complete static timing path through an input
  Starts at a clocked element in the driving device
    Referenced to a clock provided to the driving device
  Ends at a clocked element in the FPGA
    Referenced to the clock that propagates to the destination clocked element in the FPGA
  Propagates through the elements between them
    CLK > Q of the external device
    Board propagation time
    Port of the FPGA
    Combinatorial elements in the FPGA before the destination clocked element

## Slide 27: Completing the Static Timing Input Path
To complete the static timing path, you need to describe the external elements to the Vivado static timing engine
  What clock is used by the external device
  Delay between the external device’s clock and the arrival at the input port of the FPGA
    Includes the CLK > Q time of the external device and the board delay

## Slide 28: set_input_delay Command
set_input_delay command supplies the information required to complete the static timing path
  set_input_delay –clock <clock_name> <delay> <objects>
    <clock_name> is the name of the clock used by the external device
      Can be a real or virtual clock
      Can be the name of a clock; does not need to be a clock object
        Can use a clock object if desired
    <objects> is the list of objects to which to attach the set_input_delay
      Usually a set of input and/or inout ports
      Usually uses the get_ports command or the all_inputs command
    <delay> is the delay from <clock_name> to the attached <objects>
      Includes the external device and board delay
Notes: The all_inputs command (which returns a list of ports that are inputs or inouts) is convenient for applying input delays to all the input ports of the design. When this is done, the tool will usually issue a warning because the clock port is also an input port, and a set_input_delay cannot be specified on a port that has a clock attached to it. As will be indicated by the warning, the set_input_delay will not be applied to the clock port, but will be applied to all other inputs.

## Slide 29: Using a Common Clock
A set_input_delay can be related to an already existing clock
  Can be the clock attached to the FPGA clock pin
Value used for the set_input_delay is the sum of
  Clock to out of the external source
  Trace delay on the board
create_clock –name SysClk –period 10 [get_ports ClkIn]
set_input_delay –clock SysClk 4 [get_ports DataIn]

## Slide 30: set_input_delay example
create_clock –name SysClk –period 10 [get_ports ClkIn] set_input_delay –clock SysClk 4 [get_ports DataIn]

## Slide 31: Minimum and Maximum Delays
By default, each input port can have one maximum delay and one minimum delay
  Maximum delay is used for the setup check
  Minimum delay is used for the hold check
Without the –max or –min option, the value supplied is used for both
create_clock –name SysClk –period 10 [get_ports ClkIn]
set_input_delay –clock SysClk 4 [get_ports DataIn]
set_input_delay –clock SysClk –min 2 [get_ports DataIn]
Notes: Using the set_input_delay without the –max or –min option sets both the max and min to the same value. The subsequent command with the –min option overrides the min value

## Slide 32: Multiple Input Delays on the Same Port
An input can have multiple set_input_delay commands associated with it
  Use the –add_delay option
  Results in multiple static timing paths to check
set_input_delay –clock ClkA 3 [get_ports DataIn]
set_input_delay –clock ClkB 4 [get_ports DataIn] –add_delay
Notes: set_input_delay is a command that is executed in order. Without the –add_delay option, the second set_input_delay would override the first one.
Note: the two input delays define two different startpoints with their own propagation delays. The path from each start-point to the end-points in the FPGA are separate static timing paths and are each timed by the tools.

## Slide 33: Creating Input Delays Using the GUI
Timing Constraint window can be opened by selecting Window > Timing Constraints
  Clock can be created by double-clicking Set Input Delay, or a new row in the Set Input Delay table
Alternatively can be set via the Constraints Wizard
  More details to follow in this presentation

## Slide 34: Set Input Delay Wizard
Separate constraint is required for the maximum and minimum
  Wizard retains its options between invocations, making it easy to specify the minimum after the maximum has been specified

## Slide 35: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 36: Completing the Static Timing Output Path
To complete the static timing path, you need to describe the external elements to the Vivado Design Suite static timing engine
  What clock is used by the external device
  Delay between the output port of the FPGA and the external device’s clock
    Includes the required time of the external device and the board delay

## Slide 37: set_output_delay Command
set_output_delay command supplies the information required to complete the static timing path
  set_output_delay –clock <clock_name> <delay> <objects>
    <clock_name> is the name of the clock used by the external device
      Can be a real or virtual clock
      Can be the name of a clock; does not need to be a clock object
        Can use a clock object if desired
    <objects> is the list of objects to which to attach the set_output_delay
      Usually a set of output and/or inout ports
      Usually uses the get_ports command or the all_outputs command
    <delay> is the delay from the attached <objects> to the external device’s clock
      Includes the external device's requirements and board delay

## Slide 38: External Setup and Hold Requirements
External devices need a setup and hold time around the clock
  set_output_delay –max specifies the required setup time
  set_output_delay –min specifies the negative of the required hold time
create_clock –name SysClk –period 10 [get_ports ClkIn]
set_output_delay –clock SysClk 1 [get_ports DataIn]
set_output_delay –clock SysClk –min -0.5 [get_ports DataIn]
Notes: The set_output_delay values should take into account the board propagation delay.
set_output_delay –max should be the required setup time of the external device plus the longest board delay.
set_output_delay –min should be negative of the required hold time of the external device plus the shortest board delay.

## Slide 39: Complete Output Static Timing Path
Output static timing path is segmented slightly differently
  Data path delay ends at the port of the FPGA
  Destination clock path traces back through the board device to the port of the FPGA

## Slide 40: Multiple Output Delays on the Same Port
An output can have multiple set_output_delay commands associated with it
  Use the –add_delay option
  Results in multiple static timing paths to check
set_output_delay –clock ClkA 1 [get_ports DataOut]
set_output_delay –clock ClkB 2 [get_ports DataOut] –add_delay

## Slide 41: Creating Output Delays Using the GUI
Timing Constraint window can be opened by selecting Window > Timing Constraints
  Clock can be created by double-clicking Set Output Delay, or a new row in the Set Output Delay table
Alternatively can be set via Constraints Wizard
  To be covered later in this presentation

## Slide 42: Set Output Delay Wizard
Separate constraint is required for the maximum and minimum
  Wizard retains its options between invocations, making it easy to specify the minimum after the maximum has been specified

## Slide 43: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 44: Clocks for Input and Output Delay
Clock specified by the set_input_delay and set_output_delay can be any clock from the clock database
  Manually created clock attached to a clock input port of the FPGA
  Derived clock generated inside the FPGA
    This is legal, but rarely useful
Sometimes the proper clock to use does not already exist
  Virtual clocks can be created solely for the purpose of specifying input and output delays

## Slide 45: Reasons for Virtual Clocks
There are many reasons for using virtual clocks for clocking I/O
  Device external to the FPGA uses a different clock than the FPGA
    Runs at a different frequency
    Maybe a multiple/division of the FPGA clock
    Maybe the frequency of an internal FPGA clock generated by an MMCM/PLL
  Has a different delay path on the board
    Maybe has a clock buffer chip on the board
XDC provides powerful mechanisms for describing clocks
  Remember, all clocks in XDC are related by default

## Slide 46: Creating Virtual Clocks
Virtual clocks are created with create_clock
  Created clock is not attached to any design objects
  create_clock -name <name> –period <period>
    <period> is the period of the clock
    <name> is the user assigned name for the clock
  Can use the –waveform option
Can specify jitter with the set_input_jitter command
Can set clock latency with the set_clock_latency –source command
Virtual clocks are placed in the design database and can be accessed like other clocks
  Can be seen via the report_clocks command
  Can be accessed by the get_clocks command

## Slide 47: Input Static Timing Path with External Buffer
create_clock –name SysClk –period 10 [get_ports ClkIn]
create_clock –name VirtClk –period 10
set_clock_latency –source 1 [get_clocks VirtClk]
set_input_delay –clock VirtClk 4 [get_ports DataIn]

## Slide 48: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 49: The Constraints Wizard
Can only be launched after either Synthesis or Implementation
  Allows Vivado to identify and suggest timing constraints
  Writes the constraints into the XDC file via the Timing Constraints Editor
  Not mandatory but HIGHLY recommended
User flexibility
  The user has the choice to ignore the selected constraints
  The wizard can be launched even if timing constraints have already been entered into the XDC file

## Slide 50: The Constraints Wizard, Primary Clock
Defines the input clock waveform
  Object
  Name
  Frequency (MHz)
  Period (ns)
  Rise At (ns)
  Fall At (ns)
The resultant Tcl command can be previewed at the bottom of the wizard

## Slide 51: The Constraints Wizard, Generated Clocks
Vivado analyzes design to locate clocks derived from the master clock
Covers derived clocks from a main clock source
  MMCM/PLL
  Clock buffers
  GTs (UltraScale)

## Slide 52: The Constraints Wizard, Input Delays
Another way to specify Input Delays
  Identifies input signals/interfaces going into the FPGA
Defines delay parameters
  tco_min
  trce_dly_min
  tco_max
  trce_dly_max

## Slide 53: The Constraints Wizard, Output Delays
Another way to specify Output Delays
  Identifies output signals/interfaces from the FPGA
Defines delay parameters
  tsu
  trce_dly_min
  thd
  trce_dly_max

## Slide 54: The Constraints Wizard: Other Constraints
Forwarded Clocks
  The Forwarded Clocks constraint covers clock reference for output signals associated with “downstream” devices clocked by an FPGA output pin
External Feedback Delays
  Pertinent if the MMCM/PLL feedback loops used in the design is routed out of the FPGA and back into the device via input and output ports
Combinatorial Delay
  Cover paths that traverse the FPGA without being captured by any sequential elements
Physically Exclusive Clock Groups
  Define clocks that do not exist in the design at the same time
Logically Exclusive Clock Groups with No Interaction
  Define logically exclusive clocks that do not have paths between each other outside of shared sections (such as clock trees)
Logically Exclusive Clock Groups with Interaction
  Define logically exclusive clocks that have paths between each other, only clocks limited to the shared clock tree sections are logically exclusive
Asynchronous Clock Domain Crossings
  Define paths that transfer data between two clocks without a known phase relationship

## Slide 55: The Constraints Wizard: Non-Applicable Constraints
Constraints that are not applicable to the design do not have any options shown in the wizard (blank grey screen)

## Slide 56: The Constraints Wizard: Constraints Summary
The final screen of the wizard summarizes all the constraints selected for insertion into the XDC file
  Generated constraints are not immediately applied to the target XDC
  On Finish options allow for follow-up operations
    View Timing Constraints
    Create Timing Summary Report
    Create Check Timing Report
    Create DRC report using only timing checks

## Slide 57: Outline
Pin Constraints
Timing Constraints
  Period
  Input Delay
  Output Delay
  Virtual Clocks
Constraints Wizard
Summary

## Slide 58: Summary
The I/O Planner view in the Vivado IDE provides an easy-to-use interface for assigning pin locations
Use I/O Planning project for pin planning early in the design analysis
  DRC checking
  SSO analysis
  Verify I/O banking rules
Static timing paths start at clocked elements and end at clocked elements
Static timing paths are analyzed for setup and hold violations at both fastest and slowest process corners
Clocks are objects
Clocks can be created with the create_clock command

## Slide 59: Summary
set_input_delay and set_output_delay commands provide the details to complete the static timing path
set_input_delay specifies the clock of the driving component and the delay to the port
set_output_delay specifies the clock of the receiving component and the delay to the port
  –max is the required setup time
  –min is the negative of the required hold time
Port can have one –min and one –max by default
Additional delays can be specified with the –add_delay option
I/O delays can be specified with respect to virtual clocks
The Constraints Wizard is a powerful tool for creating constraints pertinent to the design